Rocky Russell Builders, Inc.

106 Regency Blvd.

Greenville, NC 27834

(252) 355-7812

DESCRIPTION OF MATERIALS

| Property Address Plan Name | 4108 Barrington Dr.. Barrington Fields Lot 85 The Roseno - REVERSED |
| --- | --- |

| Plan Square Footages: |  |
| --- | --- |
| 1st Floor Heated | 1156 |
| 2nd Floor Heated | 1346 |
| Total Heated | 2503 |
| Garage | 457 |
| Porches | 319 |
| Floor and Wall Construction: |  |
| Floor | Raised concrete slab 4” nominal thickness |
| Walls | 2x4 |
| Ceiling and Rafter | Engineered trusses |
| Wall Sheathing | ½” OSB with house wrap |
| Roof Sheathing | ½” OSB |
| First Floor Ceiling Height | 9’ |
| Second Floor Ceiling Height | 8’ |
| Insulation R Value: | E300 |
| Walls | 15 |
| Attic | 30 |
| Sound Deadening | Bathrooms, laundry room, bedroom walls adjacent to living areas |
| Plumbing, Electrical and Mechanical: |  |
| HVAC | Downstairs: 2 Ton 14 Seer Bryant Gas Furnace Upstairs: 2 Ton 14 Seer Bryant Split System Heat Pump |
| Plumbing |  |
| Bathroom Faucets | Moen Brantford (6610 Series) Satin Nickel |
| Shower Faucets | Moen Brantford (T2152) Satin Nicel |
| Bathroom Water Closets | ProFlo White (Model #PF1203WH) |
| Kitchen Sink | Sterling Stainless 33 x 22 (Model # DSE23322) |
| Kitchen Faucet/Sprayer | Pfister Satin Nickel (133 Series) |
| Garbage Disposal | 1/3 HP Badger |
| Water Heater Location | Tankless Gas Water Heater Rear Elevation |
| Tub/Shower Units Enclosure | Master Bath: Free Standing Acrylic Tub/ Tile Shower w/Framed Glass Door Guest Bath: Aquatic Tub/Shower |
| Electrical |  |
| Fireplace | 36” Direct Vent Gas (NDV4236) |
| Security System | Control panel with one keypad, one siren, door contacts on entrance doors and one motion detector. Monitoring extra charge to Buyer. |
| Stove | Electric |
| Interior Trim and Paint: |  |
| Doors (Entry) | Front: Smooth Fiberglass Rear: Smooth Fiberglass |
| Doors (Interior) | Masonite 2 Panel Arch Top Hollow Core with 3 ¼” Casing (FJ444) Satin Nickel Hinges |
| Interior Trim/Finish |  |
| Baseboard | 5 ¼” Speed Base |
| Door/Window Casing | 3 ¼” Casing (FJ444) |
| Chair Rail | Family Room, Foyer, Dining Room, & Hallway Dining To Family Room |
| Crown | 1st Floor & 2nd Floor Hallway (No Bedroom/Bathroom/Closets) |
| Wainscoting | Foyer |
| Mantel | Charlotte Mantel W/Magma Black Surround/Hearth |
| Pickets | Wrought Iron (1102/1121/1102 Per Tread) |
| Treads | Red Oak |
| Handrails | Red Oak |
| Landing | Red Oak |
| Kitchen Countertop | Purity Quartz w/ 4x8 Urban Canvas Glass Light Smoke Tile Backsplash |
| Bathroom Countertop | Bright White Cultured Marble, Recessed Oval |
| Hardware – Bathroom | Moen Mason Towel Bars, Rings, Paper Holder Satin Nickel Robe Hook Master Only Satin Nickel |
| Hardware – Doors | Kwikset Cove Satin Nickel |
| Mirrors Master Bath Guest Baths | Hanging Satin Nickel Plate Glass |
| Closet Shelving | Closetmaid PVC coated wire |
| Paint |  |
| Trim – Semigloss Latex | Three Coats (includes primer) Pure White |
| Walls – Flat | Two Coats, One Color Throughout Home Eider White (SW7014) Mega Greige (SW7031) Guest Bathrooms Tricorn Black (SW6258) Dining Room |
| Floor Covering: |  |
| Dining, Family, Kitchen, Breakfast, Foyer | Costamesa Acacia Marana Factory Hardwood |
| Bathroom Floors | Blast Statuario Tile |
| Laundry | New Castle Salt 230 Vinyl |
| Landscaping: | Bushes: Front Porch Area Only Flower Beds: Pine Straw, Front Only Grass Front: Centipede Sod Grass Side/Rear: Seeded |
| Exterior Finish Detail: |  |
| Front Porch | Per Plan, No handrails |
| Patio/Storage: | Covered Rear Porch |
| Driveway Sidewalk Rear Porch | Side entry 22’ x 20’ Pad. Remaining driveway tapered down Sidewalk from front door to parking pad in front of garage doors. 42” wide Covered Porch Only. No Screening. |
| Vinyl Siding Brick Veneer Shutters | Front/Sides/Rear Unless Brick Required Front Elevation Face Garage Wall, Face Dining Room Wall, Face Foyer Wall Per Plan |
| Shingles | 15 lb. Felt and GAF 30 Year Dimensional Weatherwood |
| Windows | Silverline Single Hung Vinyl Tilt Windows with Screens, Grill Pattern Per Plan. See attached window schedule reflecting actual window quantities and sizes used. |
| Garage Door | Carriage Style Door W/Decorative Hinges & Handles |
| Allowances: |  |
| Carpet, Pad, and Installation (Per SY) | $16.15 |
| Factory Hardwood | $5.86 |
| Vinyl | $14.65 |
| Tile | $2.50 SF |
| Lighting Can Lights (10) | $2,800.00 $600.00 |
| Kitchen Appliances Stove Model #WWFE515S0ES Dishwasher Model#WWDF320PADS Microwave Model #WWMH31017AS | $611.90 $300.15 $200.65 |

| Bricks | $0.37 |
| --- | --- |
| Mantle/Surround | $675.00 |
| Cabinets (Allowance Includes Marble Countertops) Quartz Countertop (Kitchen Only) w/Sink | $6,762.05 $2,675.00 |
| Door/Bath Hardware | $695.50 |
| Shower Enclosure | $800.00 |
| Mirrors | $275.00 |
| Windows & Exterior Doors | $5889.40 |
| Garage Door | $1,550.00 |

Actual home built may differ than printed floor plans/blueprints. Rocky Russell Builders, Inc. reserves the right to modify any printed floor plans or blueprints to account for decorator changes made by Rocky Russell Builders Inc.

All allowances include sales taxes and shipping charges unless specified otherwise.

Customer will receive credit for Allowances budgets not used.  Customer is responsible for maintaining an accounting of Allowance expenditures including any overages.  Overages are to be paid directly to Vendor by Customer prior to ordering product.  Contractor will provide Customer with a Closing Summary of Allowance Overages and Signed Change Orders at the closing of the Customer’s loan.  All Customer selections must be made with Contractor’s Approved Vendor List.

The above Allowances and Specifications have been reviewed by Customer(s):

__________________________________________		             ______________________

Customer	                                                                  Date

__________________________________________	             ______________________

Customer                                                                  Date